## Slide 1: DICOM: Testament of Time
David A. Clunie (PixelMed)
dclunie@dclunie.com
2021/12/14
ESMRMB: MRI Together workshop

## Slide 2
Speaker name:
Dr David A. Clunie, PixelMed
© David A. Clunie.
This presentation is released under a CC-BY license.
Conflicts of interest regarding this presentation:
Editor, DICOM Standard (NEMA contractor).
Various academic and commercial consulting contracts as DICOM SME.

## Slide 3
Format
http://en.wikipedia.org/wiki/More_Than_a_Feeling

## Slide 4: What is DICOM?
Open standard
Specification for interoperability
Protocol for messaging and transport
Services for storage and management
Metadata encoding mechanism
Information object definition
Information model (reflected in metadata)
Pixel data encoding mechanism (including lossless/lossy compression)
Application functionality specification and conformance mechanism
Annotation, rendering and reporting mechanisms

## Slide 5: Open Science needs Open Standards
DICOM is Open:
  publicly available and freely accessible (no fee to download, unlike ISO standards)
  freely readable (source written in open format XML DocBook)
  free to use (no license fees to implement, no commercial restrictions, no agreement)
  free of (known) external IP restrictions (theoretically procedures allow RAND not FRAND, but so far all no cost)
  free to extend (private elements, SOP Classes) (non-viral)
  free to participate and contribute to (though membership fee required to vote)
  http://en.wikipedia.org/wiki/Open_standard
High quality open source reference libraries and utilities freely available:
  dcmtk (C++)
  dcm4che (Java)
  pydicom (Python)

## Slide 6: Interoperability – Definition
“the ability of two or more systems or components to exchange information and to use the information that has been exchanged”
IEEE Standard Computer Dictionary: A Compilation of IEEE Standard Computer Glossaries. 1990

## Slide 7: DICOM Services – circa mid-90's
MR Modality
Laser Printer
Shared Archive
Workstation
Store
Store
Store
Print
Print
Q/R
Q/R
Storage Commitment

## Slide 8: DICOM Network and Media
Modality
Workstation
Store
Media
,
, ...
PC
Store
Media
,
, ...
Which Medium?
What Encoding?

## Slide 9: Why is DICOM the way it is?
Who was/is the customer?
  turnkey clinical device purchaser
Who decides?
  what goes in medical imaging device products
When did it start?
  product of the eighties – consequences

## Slide 10: Who?
Who is supported by the standard?
  clinical radiologist
  referring clinician
  research radiologist
  research scientist, engineer, physicist, etc.
  clinical trialists
  vendor engineers
Different users have different requirements
  (near) plug and play, high throughput, managed services, patient oriented, safety
  technically sophisticated, manual effort, file-oriented, research focus, specific needs
  allowing for innovation -> extensibility -> (transient) reduced interoperability
Who decides?
  vendor product managers allocate engineering resources
  focus is almost exclusively clinical – those who buy scanners, workstations, PACS, …

## Slide 14
Meyer-Ebrecht D. [Electronic Archival System for X-Rays Images - Work proposal for a research project in the
years 1974 and 1975] Elektronisches Archivierungssystem für Röntgenbilder – Arbeitsvorschlag für ein
Forschungsprojekt in den Jahren 1974 und 1975. Hamburg, Germany: Philips Research Labs; 1973 Oct.
1973

## Slide 17
1982

## Slide 18
39 years ago – radiology PACS and DICOM ubiquitous 15-20 years later!

## Slide 19: DICOM – Brief History
1982 – 1st PACS Conference – session on standards
1982 – AAPM Report 10 – Standard Format for Image Interchange
1983 – ad hoc meeting between FDA, ACR & NEMA
1983 – 1st meeting of ACR-NEMA “Digital Imaging and Communications Standards” Cmte
1985 – ACR-NEMA 300-1985 (“version 1.0”) issued
1988 – ACR-NEMA 300-1988 (“version 2.0”) issued
1990 – Inter-vendor testing of version 2.0 at Georgetown
1992 – Trial of DICOM (“version 3.0) at RSNA
1993 – DICOM 3.0 issued

## Slide 20: DICOM – Brief History
1982 – 1st PACS Conference – session on standards
1982 – AAPM Report 10 – Standard Format for Image Interchange
1983 – ad hoc meeting between FDA, ACR & NEMA
1983 – 1st meeting of ACR-NEMA “Digital Imaging and Communications Standards” Cmte
1985 – ACR-NEMA 300-1985 (“version 1.0”) issued
1985 – IEEE 802.3 Ethernet (based on 1976 Metcalfe)
1986 – Aldus TIFF (version 3; prior versions drafts only)
1987 – CompuServe GIF
1988 – ACR-NEMA 300-1988 (“version 2.0”) issued
1990 – Inter-vendor testing of version 2.0 at Georgetown
1992 – Trial of DICOM (“version 3.0) at RSNA
1992 – JPEG (ITU T.81; ISO 10918-1 1994)
1993 – DICOM 3.0 issued

## Slide 21: DICOM – Brief History
ACR-NEMA versions 1 and 2
  50-pin 16 bit parallel interface
  no network (assumed “network interface unit”)
  layered
  messages with commands and data
  tag-value pairs
  described patients, studies, images
  described modality, acquisition, 3D position, etc.

## Slide 25: DICOM – Brief History
ACR-NEMA versions 1 and 2
  50-pin 16 bit parallel interface
  no network (assumed “network interface unit”)
  layered
  messages with commands and data
  tag-value pairs
  described patients, studies, images
  described modality, acquisition, 3D position, etc.
DICOM “3.0”
  TCP/IP network protocol (and OSI semantics)
  “object-oriented” description & conformance

## Slide 26: How DICOM differs (as a file format)
DICOM dataset (PACS, message) embedded in file wrapper (PS3.10)
Clinical, acquisition and modality-specific information model
"Attributes" of "Modules" of "Information Objects" aka. metadata
Metadata to identify and describe
Metadata is embedded in each and every file
E.g., PatientName, PatientID (MRN)
Each dataset (file, instance) given a globally Unique Identifier (UID)
Grouping – commonality of higher level entity UIDs (Study, Series)

## Slide 28: What DICOM inherited from legacy formats
Major scanner vendors already had proprietary MR & CT formats
  GE Genesis (and others)
  Siemens & Philips – Standard Product Interconnect (SPI) – ACR-NEMA based
  …
One instance (file) per reconstructed slice
Binary fixed layout or tag-value pair stream
Header usually embedded with pixel data
Composite entities – patient, study, acquisition, series, instance data
What was available from operator or pulse sequence and parameters
In general, predated "volume" acquisitions (or use cases for 3D)

## Slide 29: Trying to do better – Enhanced MultiFrame
DICOM Sup 49 Enhanced MR Image Storage SOP Class (2002)
Allow multiple slices in one dataset (file)
Mechanism to factor out commonality of per-slice description
Make many more acquisition-related attributes mandatory
Make many more values standard codes (e.g., acquisition contrast)
More precise definition of timing (e.g., for perfusion)
Explicit specification of Dimensions (e.g., space, time, B value)
Separate quantitation from rendering pipeline (RWV from Windowing)
Miserable failure (MR) – significant adoption by only one vendor
Core of all new IODs, including segmentation, parametric maps

## Slide 30
Dataset (attributes+pixels)
C-Store response (acknowledgement)
C-Store request
UIDs
Store, parse, check
A s s o c i a t i o n
DB
DB
DB
DB

## Slide 31: Multi-frame Functional Groups
Per-frame attributes
Pixel data
Shared attributes

## Slide 32
Temporal Position Index
2
1
Trigger Delay Time
48 ms
0 ms
Space (2)
Time (1)
2
\
1
\
5
Dimension Index Values
Dimension Index Pointers:
Temporal Position Index
Stack ID
In-Stack Position
5
1\1\5
In-Stack Position
Stack ID = 1
4
1\1\4
3
1\1\3
2
1\1\2
1
1\1\1
5
2\1\5
In-Stack Position
Stack ID = 1
4
2\1\4
3
2\1\3
2
2\1\2
1
2\1\1

## Slide 34: Real World Value Mapping
Value
Unit
Stored
Values
Real
Value
LUT
VOI
LUT
P
LUT
Display
Real world
value
Modality
LUT
Measurement
Units Code
Sequence
(0040,08EA)
Real World
Value LUT
Data
(0040,9212)
Real World
Value Intercept
and Slope
attributes
or

## Slide 35: MR Spectroscopy
Storage of Spectroscopy Data
Metabolite Maps

## Slide 36: MR Raw Data
Email from me to NEMA dated 1993/05/16:
"It just occurred to me that the MR module in proposed DICOM 3 makes no provision for transferring the raw data."
"Now, I know that most manufacturers don't make this quite as easy to get at as the image data, but it is there and many people use it, so DICOM might as well make provision for it. This would in no way oblige manufacturers to provide it along with everything else but would make it easy for those who wanted to (key selling feature to MR physicists here). Also it would be handy for vendors implementing remote diagnostics over a network link to a DICOM compatible machine rather than through a modem hidden in a cabinet)."

## Slide 37: MR Raw Data
Not addressed in DICOM 3.0 1993
Nobody interested when followed up in 1995
By 2002 (Sup 49), consensus to encapsulate as private data elements
Raw Data IOD
  traditional patient/study/series/equipment information model attributes
  no standard payload – private elements for bulk raw data & its descriptors
  not modality-specific (i.e., can use for CT, PET, etc.)
"The Raw Data stored with the Raw Data Module consists of one or more private attributes that are vendor specific. No rules are specified about the content and format of the raw data."

## Slide 38: Store and Regurgitate

## Slide 39: MR Raw Data
Store and regurgitate has limited utility beyond archival
Researchers would obviously prefer interoperable raw data
Vendors (at least in DICOM WG 16) remain uninterested
ISMRM Raw Data (ISMRMRD) a promising start
Disappointing that ISMRMRD is not DICOM-based
Contrast with DICOM-CT-PD (projection data) developed by CT physicists for use of raw data for reconstruction challenges

## Slide 41: Quantitation and AI
Historically, many MR applications have been quantitative
Results have rarely been persisted in DICOM standard form
Screenshots saved as DICOM for human visualization
Useless semantically (not machine readable or re-usable)
Surge of (renewed) interest in AI is a new market force
Processed +/- annotated data of value for training/testing/reporting
Revitalized interest in historic and more recent DICOM mechanisms
Viewer ability to superimpose (beyond PET), e.g., parameter, heatmap
*Integration with clinical PACS using DICOM format, protocol, services

## Slide 42: DICOM encoding of ROIs
Private elements
  evil & must be stopped
Curves in image
  weak semantics, old, retired
Overlays in image
  weak semantics
Presentation States
  weak semantics, PACS favorite
Structured Reports
  best choice, but more work
RT Structure Sets
  coordinates only
Segmentations
  per-voxel ROIs; use with SR
Date | Volume | Auto LD | Auto SD
20021207 | 27080 | 49 | 27
… | … | … | …

## Slide 43: DICOM encoding of ROI Annotations
Private elements
  evil & must be stopped
Curves in image
  weak semantics, old, retired
Overlays in image
  weak semantics
Presentation States
  weak semantics, PACS favorite
Structured Reports
  best choice, but more work
RT Structure Sets
  coordinates only
Segmentations
  per-voxel ROIs; use with SR
Date | Volume | Auto LD | Auto SD
20021207 | 27080 | 49 | 27
… | … | … | …

## Slide 44: DICOM and Annotations
Relatively new things in DICOM
  Real World Value Maps
    coded way to describe voxel values (beyond Rescale Type)
    retrofitted to all existing DICOM images
    form of “annotation” that makes pixel values semantically meaningful
  Parametric Maps
    RWVM combined with floating point or scaled integer pixels
  Second-generation Radiotherapy annotations
    Conceptual Volumes – “grammar” for combining contours, segmentations

## Slide 45: DICOM and Annotations
Related DICOM IODs
  Fiducials
    markers with shape and location
  Registration
    rigid
    deformable
    well-known frames of reference (e.g., atlases)

## Slide 46: DICOM Tractography
Encoding of tracks by 3D coordinates
Coded description of what they are (anatomy)
Measurements at (subset of) points

## Slide 48: DICOM Evolves
New and updated IODs and Attributes for new technology
"Woefully archaic" (Merck 2017)
New protocols – DICOMweb (http RESTful)
New representations – XML and JSON metadata
New compression schemes (still frame and video)
New data types for bulk data – floating point pixels
New object types – parametric maps, tractography, EEG
New security mechanisms – JWT, BCP 195 (TLS)

## Slide 51: Future Direction of DICOM
DICOM could continue to be extended indefinitely
  incrementally, as historically
  backward compatibility has long been #1 priority
DICOM could be completely reconceived
  new information model
  new protocols and API
  new representations
Does being completely different but solving the same problems add value?
Do solutions for any "new" problems actually require new standard?
E.g., high speed parallel read/write of bulk (pixel) data in cloud?
  N5/Zarr style fragmentation of bulk data and separation from metadata

## Slide 52
Notes: https://carndonaghheritage.com/colgan-hall-colgan-hall-first-committee/